U1L6 Notes

Objectives:
- Describe the relationships among temperature, and volume of a gas.
- Use the combined gas law to solve problems.

Key Concepts:
- How are the pressure, volume, and temperature of a gas related?
- When is the combined gas law used to solve problems?

Vocabulary / Important:

If the temperature is constant, as the pressure of a gas increases, the volume decreases.

As the temperature of an enclosed gas increases, the volume increases, if the pressure is constant.

As the temperature of an enclosed gas increases, the pressure increases, if the volume is constant.

Boyle's law

Boyle's Law states that for a given mass of gas at constant temperature, the volume of the gas	varies inversely with pressure.

P1 * V1 = P2 * V2
..

Charle's law

Charle's law states that the volume of a fixed mass of gas is directly proportional to its Kelvin
temperature if the pressure is kept constant.

Temperature must be in Kelvin!

V1 / T1 = V2 / T2
..

Gay-Lussac's law

Gay-Lussac's law states that the pressure of a gas is directly proportional to the Kelvin	temperature if the volume remains constant.

P1 / T1 = P2 / T2

..

Combined Gas Law

The Combined Gas law describes the relationship among the pressure, temperature, and volume	of an enclosed gas.

The combined gas law allows you to do calculations in which only the amount of gas is	constant.

(P1 * V1 ) / T1 = (P2 * V2) / T2

..